# Rover Team 1

## Constraints and Task
Weight	20 Kg
Terrain Traversal	Obstacles upto 15 cm
Manual Task	Manual traversal to 3 points
	Pick up object from one location to next
Autonomous	Come to the start point automatically
	If signal is lost, come back to previous position where signal was strong

Requirements:
1. All circuits to be made in Proteus first then in ExpressPCB or Eagle
2. Mechanical CAD Design needs to be finalized
## Basic Task Layout

RF
Image Compression
GPS

## CSE (Amrit & Dhrubanka)
- RF / Wifi
  - Communication between two PC using RF
  - Establish connection between base pc and motor & arm Arduinos
- Autonomous
- Coming back to start
  - Using GPS
  - Calculating distance using wheel rotation and time
  - Mapping the whole surface?
- Signal is lost
  - Signal would probably be lost when the bot moves forward
  - Sol 1: Move back
  - Sol 2: Use GPS To store last locations and move to it
- Object Detection
  - Use Object Detection API to detect Objects
  - Using tensorflow Object Detection API for object detection, in Laptop
  - Can use openCV as well to get it color accurate as well
- Camera
  - 2 cameras?
  - One bent down for forklift and one for overview

Probable idea for base to bot communications -

- Rf module solution transfers data from one PC to another using a microcontroller (Arduino).
- w is a module that transfers data between transmitter and receiver in the 2.4ghz band.
- It can also be used to create a network tree between the transmitters and receivers.
- 5 Arduinos can be accommodated second level onwards in each level of each node(kind of like b+ tree of size 5).
- Assign proper address to each Arduino and maintain log of function at each address.
- Can use the Arduino connected to the PC (receiving data from base) as master Arduino.
- This Arduino will send data to the other appropriate Arduino based on function associated with that address.
- We will create certain header types so that it can be used to differentiate between different functions. (Ex - if I send forward arrow from my PC, then Arduino will add header ‘1’ for movement or something like that)
- Receiver Arduino will see this header and determine what Arduino to send it to.
- Separate header to serially write to PC.

Problems -
1. Each pair costs around Rs500. (Because they give range of 100m)
2. If we attach rf receiver module to the base Arduino, how will we add the nrf24l01 to the Arduino.

Further research left -
- Possibility of combining these two. (Rf and nrf24l01).
- Power consumption
- Stability

https://www.engineersgarage.com/contribution/rf-data-communication-between-two-personal-computers-part-2223

https://youtu.be/7rcVeFFHcFM (video for above link)

Connection of HC12
Github Code of user lukepereira for HC12
Forum for HC12
https://www.allaboutcircuits.com/projects/understanding-and-implementing-the-hc-12-wireless-transceiver-module/

https://youtu.be/xb7psLhKTMA(video for above link)

Probable idea for bot to base communications -

- Need to find solution for reverse communication. Rf module is not bidirectional.
- Idea - write serially to Arduino in python script during object detection like yellow ball found or something , then transfer by rf.
- Problems with idea - base Arduino already has one rf receiver and nrf24l01, can we attach another rf transmitter?
- Possible solution - https://howtomechatronics.com/tutorials/arduino/arduino-and-hc-12-long-range-wireless-communication-module/
- Claims 1000m in range and is bidirectional.
- Cost Rs1000 per pair.

Base to central arduino  -

Process -
- PC sends command(keyboard character) to arduino using serial communication(like arm control at bot last time).
- Cases defined in arduino attach a number indicating a function level (create hierarchy). Send to bot master arduino using RF module
- The bot master arduino receives the command along with the function level.
- Based on the function level, the master arduino transfers the function to the appropriate arduino.

Components -
- PCs (self made or raspi or laptop)
- Arduino
- RF (for base to bot)
- NRF24L01 (for intra bot communication) (not needed anymore, keep it in case later needed for something else)

Advantages -
- Entire motor, arm and lab network can be done directly by arduino communication
- PC will be free to execute autonomous, object detection and feed.

Problems -
- Only one way communication.
- Costly to implement network - 550 for first transceiver pair and then half for extra piece onwards (speaking of current budget)

Base Setup  -

Process -
- Script on PC gets command from pressed keyboard characters.
- PC transfers the character to arduino via serial communication.
- Arduino searches in each level array. (predefined  - map levels according to requirements)
- Attaches level to character received and sends it as an object.
- Define pin in arduino code for sending data to RF module and attach data pin in module to same pin in arduino
Doubts -
- Is it possible to send objects by arduino?
- Possible to attach function level in PC script itself and send as an object to arduino? (will reduce load of linear searching from arduino, easier to implement in python script)

Bot Master Setup -
(not needed anymore, keep it in case later needed for something else)

Process -
- RF module receives data from the base module and sends it to arduino.
- In master arduino, decipher the function and level.
- Send to appropriate arduino or to PC accordingly.

Problem -
- PC and central arduino both will need access to base motor controls (arduino for manual, pc for autonomous)
- Linear communication only. Not possible to send data from bot PC to base PC by current setups. Meaning no feedback.
For bot to base -
https://howtomechatronics.com/tutorials/arduino/arduino-and-hc-12-long-range-wireless-communication-module/
Claims 1000m range and bidirectionality.
Improvement -
Can implement feedback mechanism between arduino network since NRF24L01 is bidirectional.

Bot Network Setup -
(not needed anymore, keep it in case later needed for something else)
Process -
- All arduinos will have nrf24l01 attached to them for network creation.
- Initialise network in all of them.
- Assign address and function levels to the arduinos.
- In master arduino check function level and send to appropriate child arduino (nrf24l01 can interact with 5 others in the same level, so no need to go more than one level deep).

Problem -
- Sending results of object detection, autonomous feedback and live feed to base.
- PC also needs control on base motor during autonomous.
Improvement -
Can make make master arduino as base motor but will introduce a lot of code/functionality on a single arduino

Communication process -

Process -
- Base to bot same as mentioned above.
- Shift task assigning work from receiving arduino to pc (PC can connect to multiple arduinos using usb hub).
- Done using hc12 (solves bidirectionality problem)
- This can be used to send control commands, and receive object detection results and autonomous feedback.

Problem -
Need reliable method for video transmission.
## Electrical
### Calculations
Wheels dia=10cm
Torque (whole bot): 7.5 kgcm
We need motors of 10-15 kgcm
### GCB Design
### PCB Design

Motors to be used
ARM
- 2 stepper motors (requires 5V); 1 L298N
- 1 DC motor(Gripper) ; 1 single channel cytron
BASE
4 DC motors ; 2 dual channel cytrons

## Mechanical
### Design

## Finance

Components	Price
RF HC-12	900 Rs for Pair